## Slide 1
2-HOUR HANDS-ON WORKSHOP
Workshop on Building a Mini Vending Machine
Integrated with QRIS Payments
Live demonstration · Python application · Arduino Uno · QRIS sandbox
Presented by
Ajang Rahmat, S.Kom
Electrical Engineering · Nusa Putra University
nutral.id
Build with the supplied source code. Learn by observing, wiring, uploading, and testing.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
01

## Slide 2
01 · OPENING DEMONSTRATION
Watch the complete experience first
The instructor demonstrates the goal before explaining the parts.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
02
1
Select a product
→
2
Show the QRIS checkout
→
3
Confirm the test payment
→
4
Light the matching LED
NOTICE
The QR payment shown in the workshop must use instructor-approved sandbox credentials.
ASK
What did the application do? What did the Arduino do? Where did the QR payment fit?

## Slide 3
02 · THE PROJECT IN 5W1H
Answer the big questions before we build
Start with the purpose and user experience—not with code.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
03
WHAT?
A desktop vending interface connected to an Arduino-controlled LED demo.
WHY?
To make software, payment status, serial messages, and physical output tangible.
WHO?
A customer selects a product; an operator configures and monitors the machine.
WHERE?
Python runs on a computer; Arduino Uno runs the hardware sketch.
WHEN?
The output is requested only after the payment flow reports success.
HOW?
Python sends a serial command; Arduino maps the requested slot to an LED output.

## Slide 4
03 · SYSTEM OVERVIEW
Four parts work together
The workshop uses LEDs as a safe, visible stand-in for vending hardware.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
04
CUSTOMER
Selects a product
and scans a QR
→
PYTHON APP
Shows products,
cart, and payment
→
SERIAL LINK
Carries commands
through USB
→
ARDUINO
Turns on the LED
for the chosen slot
IMPORTANT DISTINCTION
The application, payment provider, serial connection, and output circuit are separate layers. A success message is not proof that a physical product was dispensed.

## Slide 5
04 · WHY THESE TOOLS?
Use the right tool for each responsibility
A small prototype is easier to understand when each part has one clear job.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
05
Python
Fast to read and change; coordinates the interface, cart, and payment flow.
Tkinter
Included with standard Python; creates the desktop window and buttons.
Arduino Uno
Reads a small sketch and controls hardware outputs predictably.
USB serial
Simple text messages connect the computer to the microcontroller.
QRIS sandbox
Allows a controlled payment-flow demonstration without production payments.

## Slide 6
05 · TWO-HOUR ROADMAP
A demonstration, then a guided build
Installers and hardware should be ready before the hands-on session begins.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
06
00–08
Instructor live demonstration
08–20
Project purpose and 5W1H
20–40
Install tools, create a virtual environment, install packages
40–55
Run and explore the supplied Python application
55–65
Electronics, pin map, and safety
65–80
Wire one LED; extend to three or six
80–100
Write, upload, and test the Arduino sketch
100–110
Test the serial protocol and integration path
110–115
Review and evaluation
115–120
Questions and answers

## Slide 7
06 · BEFORE THE SESSION
Prepare computers and kits
Pre-downloading installers saves hands-on time; installation and verification happen together.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
07
SOFTWARE
Python 3.11.9 (Windows installer)
Visual Studio Code
Arduino IDE
Project source folder
HARDWARE PER PARTICIPANT / TEAM
Arduino Uno and USB data cable
Breadboard and jumper wires
1–6 LEDs
One 220–330 Ω resistor per LED
INSTRUCTOR PREPARATION
Share the project source and installers in advance. Prepare a verified sandbox account for the opening demo; participants must not use production payment credentials.

## Slide 8
07 · INSTALL THE SOFTWARE
Install Python 3.11.9, VS Code, and Arduino IDE
Use official download sources; choose the Windows versions that match the classroom computers.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
08
1
Install Python 3.11.9. Enable the Python Launcher if offered.
2
Install Visual Studio Code and open the supplied project folder.
3
Install Arduino IDE and the Arduino AVR Boards / Uno support.
4
Connect the Uno with a USB data cable; note its COM port.
py -3.11 --version
Expected: Python 3.11.9

## Slide 9
08 · SET UP THE PYTHON ENVIRONMENT
Create a project-local virtual environment
Run commands in the VS Code terminal with the supplied project folder as the current directory.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
09
py -3.11 -m venv .venv
.venv\Scripts\python.exe -m pip install --upgrade pip
.venv\Scripts\python.exe -m pip install -r requirements.txt
.venv\Scripts\python.exe -c "import tkinter, serial, PIL, qrcode; print('Setup OK')"
.venv\Scripts\python.exe main.py
WHY A VIRTUAL ENVIRONMENT?
It keeps this project's packages separate from other Python projects.
IF SOMETHING FAILS
Check the current folder, Python version, and full error message before retrying.

## Slide 10
09 · EXPLORE THE SUPPLIED SOURCE
Read the project map before changing anything
Participants use the finished Python source; this workshop is not a from-scratch Python build.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
10
main.py
Connects the application flow and button actions.
vending_ui.py
Builds the Tkinter interface.
inventory.py · cart.py
Define products, stock, and cart rules.
configuration.py
Selects demo, sandbox, or production settings.
serial_controller.py
Sends commands and checks Arduino responses.
firmware/.../vending_controller.ino
Arduino sketch for the vending controller.
Goal: recognize responsibilities and follow one event across files.

## Slide 11
10 · RUN THE EXISTING APPLICATION
Start with a working baseline
Do not edit the payment configuration or copy secrets into the workshop folder.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
11
.venv\Scripts\python.exe main.py
CHECK THE APP
Window opens
Product cards and stock are visible
Select a product and observe the cart
PAYMENT DEMO
No provider key: local simulation only. With an approved sandbox key: sandbox QRIS checkout. Never scan or test production credentials in class.
SAFE PRACTICE
Keep MODE_DEMO=1 and SUMOPOD_SANDBOX=1. Do not display .env or share API keys.

## Slide 12
11 · ELECTRONICS AND SAFETY
Start with a low-voltage LED circuit
An LED is a simple output indicator; it is not a motor or a vending mechanism.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
12
ONE LED NEEDS
Arduino Uno
Breadboard
LED
220–330 Ω series resistor
Jumper wires
SAFETY RULES
Disconnect USB before rewiring. Use one resistor per LED. Never connect an LED directly to a pin. Do not connect mains voltage, motors, or relay loads in this activity.
Long LED leg = anode (+) Short leg / flat edge = cathode (−)
UNO PIN BUDGET
Each output pin drives only its own LED through a resistor. Stay within Arduino Uno pin-current limits; use the instructor-approved circuit and do not power external loads from GPIO pins.

## Slide 13
12 · WIRE THE FIRST LED
Build and inspect one complete circuit
Keep the Arduino disconnected from USB until the wiring has been checked.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
13
Arduino D2 ── 220–330 Ω resistor ── LED anode (+)
Arduino GND ─────────────────────────── LED cathode (−)
CHECK THE PATH
D2 → resistor → long LED leg → short LED leg → GND
BEFORE POWER
Check polarity, resistor placement, and that no rail is shorted.
When the one-LED test works, duplicate the circuit on D3–D7.

## Slide 14
13 · SCALE TO THREE OR SIX LEDS
One product slot maps to one output pin
Start with one LED. Add more only after the first output works.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
14
Slot 1
D2 → resistor → LED → GND
Slot 2
D3 → resistor → LED → GND
Slot 3
D4 → resistor → LED → GND
Slot 4
D5 → resistor → LED → GND
Slot 5
D6 → resistor → LED → GND
Slot 6
D7 → resistor → LED → GND
WIRING CHALLENGE
Each LED has its own resistor and its own output pin. Keep every cathode on the common GND rail.

## Slide 15
14 · WRITE THE ARDUINO SKETCH
Use the same serial protocol as the Python app
This classroom sketch drives LEDs directly with active-HIGH outputs; it is not the relay firmware.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
15
const byte LEDS[] = {2, 3, 4, 5, 6, 7};
const byte SLOT_COUNT = sizeof(LEDS) / sizeof(LEDS[0]);
void setup() {
Serial.begin(9600);
Serial.setTimeout(100);
for (byte i = 0; i < SLOT_COUNT; i++) {
pinMode(LEDS[i], OUTPUT);
digitalWrite(LEDS[i], LOW);
}
Serial.println("READY");
}
void loop() {
if (!Serial.available()) return;
String command = Serial.readStringUntil('\n');
command.trim();
if (command == "PING") { Serial.println("PONG"); return; }
if (!command.startsWith("DISPENSE,")) {
Serial.println("ERROR,UNKNOWN_COMMAND"); return;
}
int slot = command.substring(9).toInt();
if (slot < 1 || slot > SLOT_COUNT) {
Serial.println("ERROR,INVALID_SLOT"); return;
}
byte led = LEDS[slot - 1];
digitalWrite(led, HIGH);
delay(500);
digitalWrite(led, LOW);
Serial.print("DONE,"); Serial.println(slot);
}

## Slide 16
15 · UPLOAD AND TEST THE SKETCH
Compile first, then upload to the Uno
Use the USB cable, correct board, correct port, and the serial speed configured in the sketch.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
16
1
Open the sketch in Arduino IDE.
2
Tools → Board → Arduino Uno; Tools → Port → the Uno COM port.
3
Click Verify. Resolve compile errors before uploading.
4
Click Upload; wait for the upload-complete message.
5
Open Serial Monitor at 9600 baud; select Newline as line ending.
Close Serial Monitor before Python opens the same COM port.

## Slide 17
16 · VERIFY THE SERIAL PROTOCOL
Test the board before connecting the desktop app
Send each command in Serial Monitor and compare the expected response.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
17
Board startup
READY
Printed after reset
Send: PING
PONG
Board is responsive
Send: DISPENSE,1
DONE,1
D2 LED flashes once
Send: DISPENSE,3
DONE,3
D4 LED flashes once, if wired
Send: DISPENSE,9
ERROR,INVALID_SLOT
Invalid slot is rejected
Every command ends with a newline. Both sides must use 9600 baud.

## Slide 18
17 · FOLLOW THE PYTHON-TO-ARDUINO PATH
The supplied serial module checks every response
Find these functions in serial_controller.py; do not rewrite them during the workshop.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
18
serial_controller.connect("COM3", 9600)
serial_controller.check_ready() # Python sends PING; expects PONG
serial_controller.dispense(slot) # sends DISPENSE,<slot>
# waits for DONE,<slot>
serial_controller.disconnect()
PORT
Replace COM3 with the port shown by Device Manager / Arduino IDE.
PORT OWNERSHIP
Close Arduino Serial Monitor before launching the Python app.

## Slide 19
18 · OPTIONAL INSTRUCTOR-LED INTEGRATION
Demonstrate QRIS sandbox to LED output
Only the instructor should run this step with approved sandbox credentials.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
19
MODE_DEMO=0
Enables the application's dispenser path.
SUMOPOD_SANDBOX=1
Keeps the payment endpoint in sandbox.
Arduino connected
The app must receive READY and answer PING with PONG.
Sandbox payment confirmed
The selected slot LED flashes after the payment is confirmed.
STOP SAFELY
Never change SUMOPOD_SANDBOX to 0 during this workshop. Do not share API keys. Sandbox payments can still create test transactions and must use approved test credentials.

## Slide 20
19 · TROUBLESHOOTING
Check one layer at a time
Read the exact error and verify the nearest connection before changing code.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
20
Python command not found
Check Python 3.11.9 installation and the py launcher.
Package import error
Use the .venv Python executable and install requirements.txt.
Upload / COM error
Check USB data cable, board selection, port selection, and driver.
No READY / PONG
Close Serial Monitor; verify 9600 baud, newline, and the uploaded sketch.
Wrong LED lights
Compare the slot-to-pin map and check LED polarity / wiring.

## Slide 21
20 · EVALUATION
Explain the system back in your own words
Use the diagram and your successful test as evidence of understanding.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
21
PYTHON APPLICATION
Where are the products, cart rules, UI, payment configuration, and serial calls?
ARDUINO SKETCH
What do setup(), loop(), pinMode(), digitalWrite(), and Serial do?
COMMUNICATION
What does PING/PONG verify? Why does DISPENSE include a slot number?
PAYMENT AND SAFETY
When may the output happen? Why must sandbox and production credentials stay separate?
Success criteria: app runs · circuit is safe · sketch uploads · serial test passes

## Slide 22
21 · REFLECTION AND Q&A
What worked, and what would you improve?
Take one minute to reflect, then bring your questions.
MINI VENDING MACHINE · 2-HOUR WORKSHOP
22
REFLECT
Which part was easiest? Which part failed first? How did you isolate the problem?
NEXT CHALLENGE
Add three LEDs, then six. Map each product slot to one LED and confirm the serial response.
Questions and answers
Ajang Rahmat, S.Kom · Electrical Engineering, Nusa Putra University · nutral.id